## Slide 1
NEXA NET
Enterprise Network Design with Inter-VLAN Routing
Usman Haider(0074)
Nabeel Ahmad(0071)
Notes: Welcome slide. Project name is Nexa Net. Introduce the team.

## Slide 2
Project Objectives
🎯 Main Goal
Design and implement a fully functional, scalable enterprise network.
🔒 Traffic Segmentation
Segment network traffic logically by department using VLANs.
🔗 Inter-Department Communication
Enable communication between isolated departments using a router.
⚙️ IP Automation
Automate IP address assignment for all end-user devices via DHCP.
Notes: Main goal was to simulate a real-world corporate network where departments are kept separate for security but can communicate through a central router.

## Slide 3
Physical Network Topology
🌐 INTERNET
Router 2911
Core Switch 3560
HR
VLAN 10
IT
VLAN 20
Finance
VLAN 30
Sales
VLAN 40
Mgmt
VLAN 50
● PCs / Devices
Notes: Point out the core switch in the middle which connects everything. Access switches on the outside connect actual users.

## Slide 4
Topology Diagram

## Slide 5
Logical Network Segmentation (VLANs)
VLAN ID
Department
Subnet / IP Range
Gateway
VLAN 10
HR (Human Resources)
192.168.10.0 /24
192.168.10.1
VLAN 20
IT (Information Tech)
192.168.20.0 /24
192.168.20.1
VLAN 30
Finance
192.168.30.0 /24
192.168.30.1
VLAN 40
Sales
192.168.40.0 /24
192.168.40.1
VLAN 50
Management & Servers
192.168.50.0 /24
192.168.50.1
💡 /24 subnet = up to 254 usable IPs per department | Highly scalable design
Notes: Each /24 subnet gives 254 usable IPs per department, making the network scalable.

## Slide 6
Core Networking Technologies
01
Router-on-a-Stick (802.1Q)
Uses virtual sub-interfaces on a single router port to route traffic between all 5 VLANs — no extra hardware needed.
02
DHCP Pools
Router automatically leases IP addresses to PCs based on their assigned VLAN. Zero manual configuration.
03
802.1Q Trunking
Core & access switches connected via Trunk links — allows multiple VLANs to travel across a single cable.
04
Spanning Tree PortFast
Enabled on PC ports to bypass listening/learning states for immediate connectivity when a device boots.
Notes: Router-on-a-stick means we send all 5 VLANs up a single trunk cable to the router, saving hardware cost.

## Slide 7
Testing the Network (Simulation)
📸
Insert Packet Tracer
Screenshot Here
(Ping / Simulation Panel)
✅ Same-VLAN Communication
PCs within the same VLAN can ping each other successfully.
✅ DHCP IP Assignment
DHCP correctly assigns IPs to PCs — verified via 'ipconfig' on each PC.
✅ Inter-VLAN Routing
Ping from VLAN 10 (HR) to VLAN 50 (Server) passed — packet routed through sub-interfaces.
✅ DNS Resolution
www.nexanet.com resolved correctly to 192.168.50.20.
✅ Web Server Access
Browser on HR PC accessed 'Welcome to Nexa Net!' page from Web Server.
Notes: Ping from HR PC to Web Server proved the packet traveled through switches, up to the router, got routed to VLAN 50, and came back.

## Slide 8
The Benefits of This Design
📡
Broadcast Control
Performance Boost
Broadcast packets (like DHCP requests) are contained within their specific VLAN — preventing network slowdowns across all departments.
🔐
Enhanced Security
Department Isolation
By separating departments, ACLs can later restrict access — e.g., preventing Sales from reaching Finance servers.
🗂️
Logical Organization
Flexible Grouping
Employees can be grouped by department regardless of their physical location in the building.
This design mirrors best practices used in real corporate enterprise networks.
Notes: Conclude by emphasizing this setup mirrors best practices used in real corporate enterprise networks.

## Slide 9
?
Questions?
Thank you for listening!
Notes: Open floor for questions. Summarize: Nexa Net covers VLANs, DHCP, DNS, Web Server, Inter-VLAN Routing, and WiFi.